## Slide 1: Creating a Dual Subsystem Virtual Platform
Helium 22.12
Helium Training Labs

## Slide 2: Introduction
In this lab we will create a virtual platform containing 2 CPU subsystems
  The CPUs used will be ARM A55 and ARM M35
We will use the Helium Platform Assembly GUI to do this
We will not be building this platform from scratch; instead, we will re-use existing reference platforms from the Helium catalog, and modify them as necessary

## Slide 3: The platform we will create
SRAM
Router
A55
UART
GIC
A55 subsystem
Peripherals
SRAM
Router
M35
UART
M35 subsystem
Peripherals
Dual subsystem virtual platform
DDR

## Slide 4: Setting up the training materials
The training materials delivered with this Helium training require some setup before use:
  Extract the training material tarball
  Setup the tool paths and environment variables required

## Slide 5: Contents of the Training Material Tarball
Files used in ARM Fast Model creation
Pre-built software images
Software source code
Script to setup the tool paths

## Slide 6: Log in to hsv-sc48
> source /grid/sfi/farm/hsvlsf01/conf/cshrc.lsf
> bsub -Is -q interactive_vxehw -m hsv-sc48 csh
These lab materials have been tested on hsv-sc48.
  For best results, you should run these labs on hsv-sc48.
Run the following commands to get a shell on hsv-sc48:

## Slide 7: Extract the Tab Material Tarball and Setup Tool Paths
> source ${HELIUM_INST_DIR}/helium_setup.csh
> mkdir <work directory>
> cd <work directory>
> tar -xf /path/to/training/material/tarball
> cd pa_training_material
> source setup.csh
Execute the following commands in your shell:
  setup.csh sets the TRAINING_MAT_DIR environment variable which is used in the labs.
HELIUM_INST_DIR is the directory where Helium is installed

## Slide 8: Steps
Step 1 – Create the ARM Fast Models
Step 2 – Create a new platform
Step 3 – Instantiate the a53_gic400 platform
Step 4 – Replace the A53 with A55
Step 5 – Replace the GIC400 with GIC600
Step 6 – Clean up
Step 7 – Instantiate the basic_m7 platform
Step 8 – Replace the M7 with M35
Step 9 – Set run options
Step 10 – Save the platform to a catalog
Step 11 – Build & run the platform

## Slide 9: Step 1: Create the ARM Fast Models Create a catalog for the ARM models
Right click, add models to catalogs

## Slide 10: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : Create a new catalog
1. Add ARM Fast Models
2. Create a new catalog

## Slide 11: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : Name the new catalog
1. Name it ARM FM Catalog
2. Browse to a suitable location
3. Next

## Slide 12: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : Add ARMCortexA55x4 to the new catalog
1. Select the ARMCortexA55x4CT model
2. Next

## Slide 13: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : Retain the default CPU parameter values
Next

## Slide 14: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : Exclude some ports from the CPU model
2. Next
1. Browse to the CPU port exclude file in the training materials

## Slide 15: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : Finish the CPU model
Finish (the model import will take a few minutes after this)

## Slide 16: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : ARMCortexA55x4 model ready
The ARMCortexA55x4 CPU model is now ready to use

## Slide 17: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : Add the GIC600 model to the catalog
Right click, add models to catalogs

## Slide 18: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : Select the ARM FM catalog
1. Add ARM Fast Models
2. Select the ARM_FM_Catalog catalog
3. Next

## Slide 19: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : Select the GIC600 model
1. Select the GIC600 model
2. Next

## Slide 20: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : Override some GIC parameter values
2. Next
1. Browse to the GIC600 parameter file in the training materials

## Slide 21: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : Exclude some ports from the GIC model
2. Next
1. Browse to the GIC600 port exclude file in the training materials

## Slide 22: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : Finish the GIC model
Finish (the model import will take a few minutes after this)

## Slide 23: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : GIC600 model ready
The GIC600 model is now ready to use

## Slide 24: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : Add the ARMCortexM35 model to the catalog
Right click, add models to catalogs

## Slide 25: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : Select the ARM FM catalog
1. Add ARM Fast Models
2. Select the ARM_FM_Catalog catalog
3. Next

## Slide 26: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : Select the ARMCortexM35 model
1. Select the ARMCortexM35PCT model
2. Next

## Slide 27: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : Retain the default CPU parameter values
Next

## Slide 28: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : Exclude some ports from the CPU model
2. Next
1. Browse to the M35 port exclude file in the training materials

## Slide 29: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : Finish the CPU model
Finish (the model import will take a few minutes after this)

## Slide 30: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : ARMCortexM35 model ready
The ARMCortexM35PCT model is now ready to use

## Slide 31: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : Add the IDAU model to the catalog
Right click, add models to catalogs

## Slide 32: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : Select the ARM FM catalog
1. Add ARM Fast Models
2. Select the ARM_FM_Catalog catalog
3. Next

## Slide 33: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : Select the IDAU model
1. Select the IDAU model
2. Next

## Slide 34: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : Retain the default IDAU parameter values
Next

## Slide 35: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : Don’t exclude any ports
Next

## Slide 36: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : Finish creating the IDAU model
Finish (the model import will take a few minutes after this)

## Slide 37: Step 1: Create the ARM Fast Models Create a catalog for the ARM models : IDAU model ready
The IDAU model is now ready to use

## Slide 38: Steps
Step 1 – Create the ARM Fast Models
Step 2 – Create a new platform
Step 3 – Instantiate the a53_gic400 platform
Step 4 – Replace the A53 with A55
Step 5 – Replace the GIC400 with GIC600
Step 6 – Clean up
Step 7 – Instantiate the basic_m7 platform
Step 8 – Replace the M7 with M35
Step 9 – Set run options
Step 10 – Save the platform to a catalog
Step 11 – Build & run the platform

## Slide 39: Step 2: Create a new platform Create a new platform
1. Create a new platform
a55m35
2. Name it a55m35

## Slide 40: Steps
Step 1 – Create the ARM Fast Models
Step 2 – Create a new platform
Step 3 – Instantiate the a53_gic400 platform
Step 4 – Replace the A53 with A55
Step 5 – Replace the GIC400 with GIC600
Step 6 – Clean up
Step 7 – Instantiate the basic_m7 platform
Step 8 – Replace the M7 with M35
Step 9 – Set run options
Step 10 – Save the platform to a catalog
Step 11 – Build & run the platform

## Slide 41: Step 3: Instantiate the a53_gic400 platform
1. Add the new platform
2. Disable FM processing
3. Ok

## Slide 42: Step 3: Instantiate the a53_gic400 platform Rename the platform to a55_subsys

## Slide 43: Steps
Step 1 – Create the ARM Fast Models
Step 2 – Create a new platform
Step 3 – Instantiate the a53_gic400 platform
Step 4 – Replace the A53 with A55
Step 5 – Replace the GIC400 with GIC600
Step 6 – Clean up
Step 7 – Instantiate the basic_m7 platform
Step 8 – Replace the M7 with M35
Step 9 – Set run options
Step 10 – Save the platform to a catalog
Step 11 – Build & run the platform

## Slide 44: Step 4: Replace the A53 with A55 Replace core instance
1. Change instance type
3. Ok
2. Select ARMCortexA55x4CT

## Slide 45: Step 4: Replace the A53 with A55 Auto stub core.pvbus_periph_m
3. Auto stub
1. Switch to the Ports tab
2. Search for the port

## Slide 46: Step 4: Replace the A53 with A55 Connect core.core_clk*mul ports
Connect to unused_clk_mul_in

## Slide 47: Step 4: Replace the A53 with A55 Connect core.core_clk*div ports
Connect to unused_clk_div_in

## Slide 48: Step 4: Replace the A53 with A55 Connect core.ASTARTMP and core.AENDMP to 0
1. Auto stub with value
2. Set value to 0
3. OK
core.A*MP

## Slide 49: Step 4: Replace the A53 with A55 Enable GIC in the core
Change GICDISABLE parameter to false

## Slide 50: Steps
Step 1 – Create the ARM Fast Models
Step 2 – Create a new platform
Step 3 – Instantiate the a53_gic400 platform
Step 4 – Replace the A53 with A55
Step 5 – Replace the GIC400 with GIC600
Step 6 – Clean up
Step 7 – Instantiate the basic_m7 platform
Step 8 – Replace the M7 with M35
Step 9 – Set run options
Step 10 – Save the platform to a catalog
Step 11 – Build & run the platform

## Slide 51: Step 5: Replace the GIC400 with GIC600 Replace gic instance
1. Change instance type
3. Ok
2. Select GIC600

## Slide 52: Step 5: Replace the GIC400 with GIC600 Connect cpu_active_s and ppi_in ports using the Ports tab
Connect each signal of the gic.cpu_active_s[4] port to the main_reset signal
Connect the PPI ports:
  Connect gic.ppi_in_0_10 to core.CNTHPIRQ_0
  Connect gic.ppi_in_0_11 to core.CNTVIRQ_0
  Connect gic.ppi_in_0_13 to core.CNTPSIRQ_0
  Connect gic.ppi_in_0_14 to core.CNTPNSIRQ_0
  Repeat for gic.ppi_in_1_*, gic.ppi_in_2_* and gic.ppi_in_3_*

## Slide 53: Step 5: Replace the GIC400 with GIC600 Connect SPI interrupt pins
1. Select the gic.spi_in[960] array
6. Ok
4. Bind only 480 signals of the gic.spi_in port
2. Select the irqs[480] array
3. Bind them (this may take a while)
5. Add to existing binding

## Slide 54: Step 5: Replace the GIC400 with GIC600 Add a new slave port to the interconnect
2. Rename the new master to from_gic
1. Add a new master in the Masters tab of the Memory Map
3. Reconfigure the interconnect

## Slide 55: Step 5: Replace the GIC400 with GIC600 Connect the new interconnect port to the GIC
1. Connect ps_router.from_gic to gic.pvbus_m
2. Allow Helium to add a bus width converter

## Slide 56: Step 5: Replace the GIC400 with GIC600 Connect the GIC to the CPU
Unbind core. gicv3_redistributor_s_pvbus_s
and core. gicv3_redistributor_s_pvbus_m

## Slide 57: Step 5: Replace the GIC400 with GIC600 Connect the GIC to the CPU
Connect core. gicv3_redistributor_s_pvbus_s to gic.redistributor_m_pvbus_m
Connect core. gicv3_redistributor_s_pvbus_m to gic.redistributor_m_pvbus_s

## Slide 58: Steps
Step 1 – Create the ARM Fast Models
Step 2 – Create a new platform
Step 3 – Instantiate the a53_gic400 platform
Step 4 – Replace the A53 with A55
Step 5 – Replace the GIC400 with GIC600
Step 6 – Clean up
Step 7 – Instantiate the basic_m7 platform
Step 8 – Replace the M7 with M35
Step 9 – Set run options
Step 10 – Save the platform to a catalog
Step 11 – Build & run the platform

## Slide 59: Step 6: Clean up Remove unnecessary sockets
Delete unnecessary sockets

## Slide 60: Steps
Step 1 – Create the ARM Fast Models
Step 2 – Create a new platform
Step 3 – Instantiate the a53_gic400 platform
Step 4 – Replace the A53 with A55
Step 5 – Replace the GIC400 with GIC600
Step 6 – Clean up
Step 7 – Instantiate the basic_m7 platform
Step 8 – Replace the M7 with M35
Step 9 – Set run options
Step 10 – Save the platform to a catalog
Step 11 – Build & run the platform

## Slide 61: Step 7: Instantiate the basic_m7 platform
1. Select the topmost a55m35 node in the Design Editor
2. Add basic_m7 platform
3. Disable FM processing
4. Ok

## Slide 62: Step 7: Instantiate the basic_m7 platform Rename the platform to m35_subsys

## Slide 63: Steps
Step 1 – Create the ARM Fast Models
Step 2 – Create a new platform
Step 3 – Instantiate the a53_gic400 platform
Step 4 – Replace the A53 with A55
Step 5 – Replace the GIC400 with GIC600
Step 6 – Clean up
Step 7 – Instantiate the basic_m7 platform
Step 8 – Replace the M7 with M35
Step 9 – Set run options
Step 10 – Save the platform to a catalog
Step 11 – Build & run the platform

## Slide 64: Step 8: Replace the M7 with M35 Replace core instance
1. Change instance type
3. Ok
2. Select ARMCortexM35PCT

## Slide 65: Step 8: Replace the M7 with M35 Instantiate IDAU
1. Select m35_subsys
3. Rename the instance to IDAU
2. Add IDAU

## Slide 66: Step 8: Replace the M7 with M35 Connect IDAU to the M35
Connect core.idau to IDAU.pvbus_s
Connect core.idau_invalidate_region to IDAU.invalidate_region

## Slide 67: Step 8: Replace the M7 with M35 Stub unused ports
Stub these ports of the M35 core:
  core.intnum: auto-stub
  core.stcalib[2]: auto-stub with value 0
  core.initsvtor, core.initnsvtor: auto-stub with value 0

## Slide 68: Step 8: Replace the M7 with M35 Delete unnecessary sockets and models
Delete unused_dap_s and unused_ahbd
Delete ahbp_m_64_32 and ahbs_32_64

## Slide 69: Step 8: Replace the M7 with M35 Delete unnecessary peripherals and masters in the memory map
2. Delete ahbp_m (in Masters) and m7_ahb_s_tcm (in Peripherals)
1. Select the ps_router in the m35_subsys
3. Reconfigure the router connections

## Slide 70: Step 8: Replace the M7 with M35 Add an SRAM instance
2. Add a simple_memory_32 instance
1. Select the m35_subsys
3. Rename it to sram

## Slide 71: Step 8: Replace the M7 with M35 Add the SRAM to the memory map
1. Add the SRAM to the memory map
2. Reconfigure the router

## Slide 72: Step 8: Replace the M7 with M35 Connect the SRAM reset pin
Connect sram.reset_in to main_reset

## Slide 73: Step 8: Replace the M7 with M35 Set up the memory map
1. Adjust ranges:
SRAM: Start = 0x00000000, Size = 0x00010000
DDR: Start = 0x20000000, Size = 0x00020000
DMA: Start = 0x4c010000, Size = 0x00001000
UART0: Start = 0x4c000000, Size = 0x00001000
2. Reconfigure the router connections

## Slide 74: Steps
Step 1 – Create the ARM Fast Models
Step 2 – Create a new platform
Step 3 – Instantiate the a53_gic400 platform
Step 4 – Replace the A53 with A55
Step 5 – Replace the GIC400 with GIC600
Step 6 – Clean up
Step 7 – Instantiate the basic_m7 platform
Step 8 – Replace the M7 with M35
Step 9 – Set run options
Step 10 – Save the platform to a catalog
Step 11 – Build & run the platform

## Slide 75: Step 9: Set run options Set run options
-cciparam a55m35.a55_subsys.loader.source0=`heliumlib`/releasecatalog/cadence.com/software/vexpress_simple_soc/images/linux-armv82-gic600.axf
-cciparam a55m35.a55_subsys.loader.source1=`heliumlib`/releasecatalog/cadence.com/software/vexpress_simple_soc/images/boot-armv8.bin
-cciparam a55m35.a55_subsys.loader.destination1=0x0
-cciparam a55m35.m35_subsys.loader.source0=${TRAINING_MAT_DIR}/images/cpuinfo.elf
TRAINING_MAT_DIR is set by the setup.csh script accompanying the training materials for this lab

## Slide 76: Steps
Step 1 – Create the ARM Fast Models
Step 2 – Create a new platform
Step 3 – Instantiate the a53_gic400 platform
Step 4 – Replace the A53 with A55
Step 5 – Replace the GIC400 with GIC600
Step 6 – Clean up
Step 7 – Instantiate the basic_m7 platform
Step 8 – Replace the M7 with M35
Step 9 – Set run options
Step 10 – Save the platform to a catalog
Step 11 – Build & run the platform

## Slide 77: Step 9: Save the platform to a catalog Save to catalog
Create a new catalog
Give it a name and browse to any directory for its location. Remember this directory, it will be used later.
Name the platform a55m35
Name the platform variant vdefault

## Slide 78: Steps
Step 1 – Create the ARM Fast Models
Step 2 – Create a new platform
Step 3 – Instantiate the a53_gic400 platform
Step 4 – Replace the A53 with A55
Step 5 – Replace the GIC400 with GIC600
Step 6 – Clean up
Step 7 – Instantiate the basic_m7 platform
Step 8 – Replace the M7 with M35
Step 9 – Set run options
Step 10 – Save the platform to a catalog
Step 11 – Build & run the platform

## Slide 79: Step 10: Build & run the platform (GUI) Build and run the platform from the GUI
1. Build the platform
2. Run the platform

## Slide 80: Step 10: Run output
M35 subsystem UART output
A55 subsystem UART output

## Slide 81: Step 10a: Build & run the platform (command line) Build and run from the command line
To build and elaborate the platform:
  make -f <catalog directory>/<catalog name>/cadence.com/platform/a55m35/vdefault/makefile elab
To run the platform:
  make -f <catalog directory>/<catalog name>/cadence.com/platform/a55m35/vdefault/makefile run
Note:
  <catalog directory> is the directory where you created a catalog in Step 9 previously.
  <catalog name> is the name you gave the catalog (with spaces replaced with underscores) in Step 9 previously.