## Slide 1: Helium SW Debug Training

## Slide 3: Embedded Software Debug Features and Flows
Flows and High Level Features
Native Interactive embedded software debug on virtual cores: Symbolic debugging for debug-built (-g) images and disassembly debugging for all images. Debug bare metal programs, 32-bit and 64-bit Linux including kernel modules and Android. Will extend to Linux applications in the future. Supported for ARM virtual cores (SystemC). Support for other cores coming in future releases.
Native Interactive embedded software debug on RTL cores: With support for debug on ARM v9-a, v8-a, v7-m RTL cores (Xcelium simulation, Palladium, Protium). More ARM architectures and cores coming in future releases.
Multi-core and multi-process software debugging in same design.
RTL Register and Memory Access at Software Breakpoints
Synchronized Debug on Virtual and RTL cores
Integrated Software Debug and Signal Level scripting for automation of Hardware and Software tests
Full-featured Software Debug GUI based on Eclipse CDT including Helium-customized views for:
Processor/Core Selection and Stack Frame Management in Debug View.
Examining core registers for both virtual and RTL cores in dedicated Register View.
Viewing source code disassembly with ability to show side-by-side with source, instruction step or source step, set breakpoints in Disassembly View.
Source code editing with powerful C/C++-aware Source Code View. Outline View for syntax-based navigation.
Viewing local variables and parameters in Variables View and other variables and expressions in Expressions View.
Debugger access to the memory of virtual and RTL models. View and change memory values in configurable Memory View.
Browsing source files of images in Helium Image Browser View.
Examining parameters, registers, and ports of virtual components in Helium System View.
Breakpoint management, including process and core specific breakpoints, conditional breakpoints, hardware breakpoints, watchpoints, Breakpoint View.
Issuing debug commands in Interactive Console View synchronized with GUI.
Managing debug sessions, run-time options and configuring software images using debugger configuration files in Images/Symbols View.
Embedded software debug scripting language integrated with RTL/SystemC scripting: Includes scripting language with full suite of symbolic debug operations, processor control and kernel module debug.
Support for debugging Linux kernel modules: Helium built-in knowledge of Linux internal data structures enable kernel debug

## Slide 4: Example Overview
After product setup, you can run examples illustrating software debugging
  Some of the platforms in `xmroot`/tools/esl/modelcatalog/releasecatalog are setup to show how to use the Helium Debugger
    vexpress/a35_m7_gic400_hybrid
    vexpress_v9/klein_gic600_ufs
    vexpress_v9/matterhorn_gic700_virtio
  Examples include README and RUNME files - See README files for complete instructions to use.

## Slide 5: Agenda
Overview - Helium SW Debugger
Launch - Helium SW Debugger
  Tools Setup & Helium Invocation Commands
  Getting started with: Arm-v9 Hybrid Platform
Preparing - Helium SW Debug Configurations
  Debug Configuration - Create ,Manage and Run
  ESW Configuration File Overview (Images/Symbols)
Connecting - Helium SW Debugger
  Two Connection Approaches based on debug use cases
  Working With an RTL Platform
Debugging - SW Debug Perspective
  Overview of Helium SW Debug GUI
  Debugging Features
SW/HW Debug Scenarios
  How to Debug a Hang
  Debugging Linux
  Debugging Platforms
Command Language and Scripting
Save to Catalog
Add / Remove Virtual Models
Parameter Config / Port Binding
Rewire Interrupt and Memory Map
Add / Remove RTL Stubs
Hybrid Adaptors & RTL Connection
RTL Sidechanges
Notes: Review items #3,4 to some more meaningful title.
[ankit]: Think if sub-section can be deleted: Tools Setup & Helium Invocation Commands

## Slide 6: Overview - Helium SW Debugger

## Slide 7: Helium Unified Software Debug Across Runtime Engines
SoC
DDR3
Display
INTC
Timer
CSI
DSI
UART
GPU
MC
SATA
USB3
…
System
Boot
USB2
Ethernet
Mem
IP 2
CPU
CPU
SoC
DDR3
Display
INTC
Timer
CSI
DSI
UART
GPU
MC
SATA
USB3
…
System
Boot
USB2
Ethernet
Mem
IP 2
CPU
CPU
SoC
DDR3
Display
INTC
Timer
CSI
DSI
UART
GPU
MC
SATA
USB3
…
System
Boot
USB2
Ethernet
MMP
IP 2
CPU Sub-system
CPU Sub-system
OS
SoC Drivers
Software Tests
Variable View
Breakpoints
Core specific Stack View
Memory View
Mixed Abstraction Software Debug
Multi-core, multi-processor Debug
Customized System View
Powerful TCL scripting with HW & SW visibility
Hardware-Software Command Console
Palladium
Protium
Xcelium
Linux Kernel Module Debug
Dynamic Disassembly
Register View
Live RTL IP Register Values
Helium

## Slide 8: Key Embedded Software Debug Features
Full-featured Interactive Software Debug Capabilities (derived from Eclipse CDT)
Multi-Core and Multi-Processor Debugging in same session
Native Interactive embedded SW debug on virtual and/or RTL processor cores
System View to examine virtual components and registers (and parameters)
Current Debug State (current stop reason, location, number of instructions, etc.)
Full-featured scripting language integrated with hardware debugging commands
Debugger access of memory in virtual or RTL models
Native integration with runtime engines (Helium, Xcelium, Palladium, Protium)
  Full-featured Software debug scripting integrated with hardware debug scripting in tcl
  Live debug view of addresses whether mapped to virtual or RTL components
  Synchronization between software and hardware run and stop
Support for debugging Linux kernel modules

## Slide 9: Launch - Helium SW Debugger

## Slide 10: Tools Setup & Invocation - Helium SW Debug GUI
Invoke Command:
  > helium &
A dialog to select a workspace will appear
  Select a new workspace when using helium for the first time
  On subsequent runs, workspaces created with helium can be selected with the drop-down arrow
Tools Setup & License :
  > source /lan/cva_rel/helium21h1/21.05.s001/helium_setup.csh
Notes: Merge these multiple slides and clean-up – Done
[Ankit] – 09/08 – Following text removed for Basic Training. Review if this is required to keep.
Interactive Command Line Debug
  > xrun –helium –esw <esw_option> -tcl …
Scripted Debugging
  > xrun –helium –esw <esw_option> -input <scripting file> …

## Slide 11: Select - Helium SW Debug Perspective
1. Default view -> Platform Assembly
2. Switch to -> Helium Software Debug Perspective
Helium Software Debug Perspective (Default View)
This icon can be used to switch back to Helium Platform Assembly
Notes: [Ankit] – Added. Confirm if its ok. Also added pic in next slide. Decided what is better to show and update slide accordingly. Remove highlighted if we keep next slide.

## Slide 12: Getting started with Example: Arm-v9 Hybrid Platform
2. Choose Any Example from Helium Model Catalog Platforms
4. Select the shown options to run on Xcelium
3. Double click to Open Platform
5. Click on Finish
1. Switch to Helium Platform Assembly View
2
1
3
4
5
Built-in Examples

## Slide 13: Getting started with Example: Arm-v9 Hybrid Platform
Build ARM-FM
After clicking on “Finish”
Platform Opened In Design Editor
After successful Fast model build, Platform will be opened in Design Editor
Build Platform
Click on Project -> Build Platform
Run Platform
Start Building Fast Models present in Platform
Click on Run -> Run Platform
Default Test -> Hello World
Platform is Ready to setup “Debug Configurations”

## Slide 14: Preparing - Helium SW Debug Configurations

## Slide 15: Debug Configuration
Debug Configurations are used to set platform run options and select software images to run
Helium Software Debug contains commands and options required to run platforms
The Images/Symbols tab provides an editor to create or update the Debugger Configuration File
A single platform can contain multiple Debug Configurations to run with different hardware and software options

## Slide 16: Preparing - Helium SW Debug Configurations
What is Debug Configuration?
  In the Helium Embedded Software Debug tool, you can create a “debug session” by providing run options and provide a reference software image and symbols to start SW debugging
  You can name the debug session based on need.
Create, Manage and Run – Such Multiple Debug Configurations
Helium Software Debug
ESW Configuration File (Images/Symbols)
Notes: [Ankit] – new slide added. Show this section live in Demo, when ever necessary.

## Slide 17: Preparing - Helium SW Debug Configurations
Helium Software Debug
Click on Run -> Debug Configuration
Double-click on the “Helium Software Debug” text in the left pane
Provide Name of configuration
Provide Run Directory Path
Entering a command in the “Run Command” text box to invoke xrun
Selecting the Platform, will pre populate ‘Run Directory’, ‘Run Command’, ‘Extra Run Arguments’ which were utilized for Platform Bring up
You can press the Apply button to save settings
Click on Debug button to launch the Debug Configuration which named as “New_configuration”

## Slide 18: Preparing - Helium SW Debug Configurations
Helium Software Debug
Click on Run -> Debug Configuration
Double-click on the “Helium Software Debug” text in the left pane
Provide Name of configuration
Provide Run Directory Path
Enter a command in the “Run Command” text box to invoke xrun from script
Selecting the Platform, will pre populate ‘Run Directory’, ‘Run Command’, ‘Extra Run Arguments’ which were utilized for Platform Bring up
You can press the Apply button to save settings
Click on Debug button to launch the Debug Configuration which named as “New_configuration”

## Slide 19: Preparing - Helium SW Debug Configurations
Click on Run -> Debug Configuration
Double-click on the “Helium Software Debug” text in the left pane
Provide Name of configuration
Provide Run Directory Path
Enter a command in the “Run Command” text box to invoke xrun from script
Selecting the Platform, will pre populate ‘Run Directory’, ‘Run Command’, ‘Extra Run Arguments’ which were utilized for Platform Bring up
You can press the Apply button to save settings
Click on Debug button to launch the Debug Configuration which named as “New_configuration”
Helium Software Debug

## Slide 20: Preparing - Helium SW Debug Configurations
Click on Run -> Debug Configuration
Double-click on the “Helium Software Debug” text in the left pane
Provide Name of configuration
Provide Run Directory Path
Enter a command in the “Run Command” text box to invoke xrun from script
Selecting the Platform, will pre populate ‘Run Directory’, ‘Run Command’, ‘Extra Run Arguments’ which were utilized for Platform Bring up
You can press the Apply button to save settings
Click on Debug button to launch the Debug Configuration which named as “New_configuration”
Helium Software Debug

## Slide 21: Preparing - Helium SW Debug Configurations
Click on Run -> Debug Configuration
Double-click on the “Helium Software Debug” text in the left pane
Provide Name of configuration
Provide Run Directory Path
Enter a command in the “Run Command” text box to invoke xrun from script
Selecting the Platform, will pre populate ‘Run Directory’, ‘Run Command’, ‘Extra Run Arguments’ which were utilized for Platform Bring up
You can press the Apply button to save settings
Click on Debug button to launch the Debug Configuration which named as “New_configuration”
Helium Software Debug

## Slide 22: Preparing - Helium SW Debug Configurations
Click on Run -> Debug Configuration
Double-click on the “Helium Software Debug” text in the left pane
Provide Name of configuration
Provide Run Directory Path
Enter a command in the “Run Command” text box to invoke xrun from script
Selecting the Platform, will pre populate ‘Run Directory’, ‘Run Command’, ‘Extra Run Arguments’ which were utilized for Platform Bring up
You can press the Apply button to save settings
Click on Debug button to launch the Debug Configuration which named as “New_configuration”
Helium Software Debug

## Slide 23: Preparing - Helium SW Debug Configurations
Why do we need a ESW Configuration File?
A ESW Configuration File is a single place to specify software related associations. It specifies:
    Names of processors and sub-cores
    Location of associated source code/images/symbols to load and their loading mechanisms
    Connection information to the virtual CPU
    Connection information to the RTL CPU (RTL BFM path, protocol, etc.)
Specify the Configuration File to xrun using this option:
    -esw config:<path_to_configuration_file>
ESW Configuration File (Images/Symbols)

## Slide 24: Preparing - Helium SW Debug Configurations
ESW Configuration File (Images/Symbols)
Select the Config file using the browse button.
Save a copy of Configuration
Refresh the processor, core data from the source platform when the platform is open in an editor.
Add Symbol File
Add Images
Edit Images
Remove

## Slide 25: Preparing - Helium SW Debug Configurations
Multiple Debug Configurations can be maintained and then selected/edited in the GUI
  Create, Manage and Run – Such Multiple Debug Configurations
A single platform can contain multiple Debug Configurations to run with different hardware and software options
Helium Software Debug
ESW Configuration File (Images/Symbols)

## Slide 26: Arm-v9 Hybrid Platform Example- Configuration File Processors section: virtual CPU
processor {
name vexpress_v9.core
abstraction virtual
image {
load /path/to/linux-system.axf
symbolfile /path/to/vmlinux
loader vexpress_v9.loader
source /path/to/linux/src/dir
}
cores {
core {
name vexpress_v9.core.cpu0
coretype armv9a
}
core {
name vexpress_v9.core.cpu1
coretype armv9a
}
core {
name vexpress_v9.core.cpu2
coretype armv9a
}
core {
name vexpress_v9.core.cpu3
coretype armv9a
}
}
}
Configuration file fragment
Helium GUI

## Slide 27: Processors section: RTL CPU
processor {
abstraction rtl
bfm
{
path tb_top.a76_apb_bfm
type apb
adapter dpi
}
image {
load /path/to/linux-system.axf
symbolfile /path/to/vmlinux
source /path/to/linux/src/dir
}
cores {
core {
name platform_name.RTLProcessor0.cpu0
coretype a76
}
core {
name platform_name.RTLProcessor0.cpu1
coretype a76
}
core {
name platform_name.RTLProcessor0.cpu2
coretype a76
}
core {
name platform_name.RTLProcessor0.cpu3
coretype a76
}
}
Configuration file fragment
Abstraction is RTL
Debugger BFM RTL path and protocol
Notes: [Ankit] 16-sep – Add real example from n2

## Slide 28: Processor/Gearshift Configuration File Syntax
config {
<processors_section>
[<gearshift_section>]
}
<processors_section> ::=
processors {
[<processor_info>]…
}
<gearshift_section> ::=
gearshift {
[<gearshift_group>]…
}
Standard hybrid configuration
New for Gear Shift

## Slide 29: Processors Section
<processor_info> ::=
processor {
name <processor_name>
abstraction <abstraction_type>
[<bfm_info>]
[<image_info>]
<cores_section>
}
Name for display in GUI and use in TCL commands
Either virtual or RTL
Specifies the BFM that can be used for debugger queries
Path to images to load, loading mechanism, path to symbol info, source code, etc.
Provides information about names and number of cores within processor

## Slide 30: Additional RTL processor related information
<bfm_info> ::=
bfm {
path <path_to_bfm_instance>
type <bfm_type>
[adapter <adapter_type>]
}
Adapter used to communicate with the BFM
One of dpi or vdi
Note: dpi is optimized for debug
The protocol to use when communicating with the BFM
One of apb, ahb, axi or jtag
Note: apb has high performance
RTL path of a BFM that can be used for debugger queries
Notes: [Ankit ]Dpi or vdi – Confirm this with R & D
[Ankit] - apb, ahb, axi or jtag – Call out for performance and what is best for Helium

## Slide 31: Cores Section
<cores_section> ::=
cores {
[<core_info>]…
}
<core_info> ::=
core {
name <full_path_name>
coretype <core_type> |
<core_name>
}
<core_type> := armv8a | armv7m
<core_name> := a76 | a53
To use gearshift, specify a <core_name> instead of <core_type>. Helium needs to know the exact core and not just the architecture.
<full_path_name> must include processor portion of the path. E.g. processor1.cpu0
Lists the names and types of the individual cores which are part of the processor

## Slide 32: The –esw option to xrun
Syntax: -esw config:<config_file>
  The config file will identify virtual/RTL processor paths, connection type (e.g. VDI/APB) for RTL cores, other needed information to configure connection to RTL
  If config file is specified multiple times only first occurrence is processed
Notes:
  -esw option values also serves today to prepare databases for Indago ESWD – that use model is not supported with Helium
  Usage of –esw as above enables all Helium command/debug engine support and requires Helium licenses

## Slide 33: Connecting - Helium SW Debugger
Notes: [Ankit] 09/08 – title changed from “Connection to Simulation for Software Debug” to

## Slide 34: Based on Use cases
Helium SW Debug Config Launch
Launching the session is closely tied and under the Control of the Helium SW Debugger
Walk Up Connection
Connect to already Running Simulation on PZ1/PZ2 or Protium
Detach simulation from Helium SW Debugger on the Go without killing the run and continue simulation
Remote Host connection
Customize the commands quickly in GUI before launch
Create/Save customized Run, Debug settings associated with a given platform
Change software images, associated symbols using the Images/Symbols tab and launch multiple SW runs without closing the GUI.
This approach allows interactively setting breakpoints at points of interest before starting the debug session
Attach simulator to Helium SW Debugger by selecting PID from the prompted window
Debugging Symbols (e.g. vmlinux) and source code location information can be added after attachment using the esw Tcl command
On Demand connect with Helium SW debugger after reaching the simulation run to an interested point
Notes: [Ankit]: Confirm Protium

## Slide 35: Based on Use cases
Click on Run -> Debug Configuration
Once Debug Configuration is prepared, click on “Debug” button to connect to Helium SW Debugger
Helium SW Debug Config Launch
Notes: [Ankit]: Confirm Protium

## Slide 36: Based on Use cases
Once the connection is established successfully -> Helium SW Debugger Perspective
We are ready to start SW Debug !
Helium SW Debug Config Launch
Notes: [Ankit]: Confirm Protium

## Slide 37: Based on Use cases
Run the simulation using “command line” from terminal
Stop the run to the point of interest to start SW Debug
Open Helium GUI with ‘helium &’ command from any terminal
  Meaning both Helium and Simulation are invoked independently
  No need to add catalog OR open platform in Helium
Change the perspective by clicking on Window-> Perspective -> Open Perspective -> Helium Software Debug
Click on “Run -> Attach to Simulation”
You will be prompted with following “Attach To Process” dialog box.
Select the PID of your run and click on “Connect”
You can Detach from Simulator once done with debug
Walk Up Connection
Notes: [Ankit]: Confirm Protium

## Slide 38: Based on Use cases
Depending on when the simulation is stopped, we can see the C files and disassembly view accordingly
Enter esw commands in helium Console to provide path to Image and source dir, if not already set
  esw –image /path/image.axf
  esw –source /path_of_source_code
  esw –describe -> will show the basic info of the design
  esw –help -> to see command help. Refer to User Guide for more details
Use Buttons to point to Images, if prompted
Walk Up Connection
Notes: [Ankit]: Confirm Protium

## Slide 39: Debugging – Helium SW Debug Perspective
Notes: Consider making this content an interactive part of the labs

## Slide 40: Default Layout Overview
Session Controls
System View
Image and File Browser
Registers View
Breakpoint Manager
Current Core Selection
Disassembly Viewer
Variables Viewer
Command Console
Source Files
Viewer/Editor
Core Selection and Context
Memory Viewer

## Slide 41: Processor/Core Selection and Stack Frame Management
Debug View provides tree of processor and cores available in system
Select different processor/core or stack frame to change active debug context.
Change of active debug context impacts other views like Variables, Disassembly, Editor and updates the current status of Debug context

## Slide 42: System View Basics
Register groups provides access to registers. Registers are presented by bank name.
Expand register bank and select interesting register to get value in different formats
To change value of register select register, in selected row click in Value column, edit, press Return to confirm new value or Esc to cancel
If register value has changed since last stop it will be visible with yellow background. If simulation is running values are not updated and it is not possible to change value
System View: Provides access to different components associated with a CPU:
- Properties, peripheral registers and CCI parameters

## Slide 43: Image File Browser View - Overview
Image File Browser helps navigate between source files
Image File Browser presents list of source files with functions related to image for selected CPU
If Image File Browser is empty make sure that image is associated with selected CPU
Important: CPU is selected using Debug View

## Slide 44: Commands for software debug in existing Xcelium/Xedebug command language
In addition to interactive debugging using the Eclipse GUI, a full featured command language is available for use in the console, or without the GUI.
Basic Command syntaxes
  esw [<processor_list> | -all | -any | <osname>] <command_option> [<command_arguments>]…
    Software debugging applied to given processors
  run [<processor_list> | -all | -any | <osname>] <command_option> [-istep,-sstep,-snext,sfinish]
    Software stepping applied to given processors
  stop –esw <processor_list> <command_options>
    Mix SW/HW conditions and actions
Use esw –help to see available command options and syntaxes

## Slide 45: Simulation Control
You can control simulation using selected options from toolbar.
Toolbar contains information about current simulation status and reason of stop in case of breakpoint or watchpoint hit
Available options depends on current status of simulation
To use stepping based on source code(default), make sure that image is associated with selected CPU
Resume
Suspend
Terminate

## Slide 46: Simulation Control
Click on Step Into to run simulation until it reaches next line of code to execute
Click on Step Over to run simulation until it reaches next line of code in current functions.
Click on Step Out to continue simulation until end of current function
By default, Step actions based on lines of source code. Instruction Stepping Mode is enabled in Debug View, single instructions are executed instead of lines from source code
Important: To use stepping based on source code, make sure that image is associated with selected CPU
Step Into
Step Over
Step Return
Instruction Stepping Mode

## Slide 47: Simulation Control - Commands
run -sstep run single line of code
run -snext run single line of code if current line is subroutine call, treat it as single instruction
run -sfinish run until end of current function
run -istep run single instruction
exit terminate simulation

## Slide 48: Breakpoint Management
There are various methods to manage breakpoint actions:
  Eclipse Views/Tabs
    Image File Browser
    Breakpoints Tab
    Outline
    Disassembly
    Source
    Memory
  Tcl commands: esw, stop, …
Breakpoint actions include:
  Setting breakpoint
  Disable/Enable breakpoint
  Delete breakpoint

## Slide 49: Breakpoint Management – Commands related to Breakpoints
To set a software breakpoint using the command language:
  esw -break [<symbol_name> | <file_name>:<line_num> | <address>] [ -hw | -sw | -auto]
A breakpoint number will be displayed
This breakpoint number can be used in subsequent commands:
  esw –disable | -enable | -delete <number>
To see all breakpoints
  esw –info break
To make a breakpoint conditional:
  esw –cond <number> <condition_expression>
Ignore a breakpoint
  esw –ignore <number> <count>

## Slide 50: Disassembly View
If view is not visible select Window -> Show View -> Disassembly
  Setting instruction stepping mode will also show view automatically
Line with arrow on left side and instruction on green background represents current PC value
Previous instructions are on lighter green background
Useful for debugging the optimized Code
Use scrollbar to navigate

## Slide 51: Registers View
CPU name is visible on top of view on left side
It is possible to check actual value of a register or different properties like access mode or description (if available)
Expand register bank and select interesting register to get value in different formats
To change value of register select register, in selected row click in Value column, edit, press Return to confirm new value or Esc to cancel

## Slide 52: Variables View
Accessibility of variables depends on compilation settings and some variables may not be accessible
  Variables available at current call stack location are displayed
  You can change selection in Debug View
Select interesting variable to get value in different formats
To inspect fields of complex types like structure, expand the variable
To change value of variable, select corresponding row, in selected row click in Value column, edit, press Return to confirm new value or Esc to cancel ; it may not always be possible to change value due to compiler settings

## Slide 53: Expressions View
If view is not visible select Window -> Show View -> Expressions
  View is not present in default initial layout, but adding it during a session will add for future sessions
Expression can be single variable, register or combination of both using most C operators (however, function calls are not supported)
Register should be referenced using full path
To add expression click on Add New expression row

## Slide 54: Memory View Basics
Memory view provides access to selected memory region by creating Memory Monitors
  As seen from processor selected at time of Memory Monitor Creation
    If processor has MMU turned on, the memory is using virtual addresses
It is possible to check selected memory address or use different source like Variables View
Memory view provides option to create watchpoint
In a hybrid platform, memory range may map to RTL devices
  Viewing such memory may cause side-effects as RTL needs to run for evaluation
Notes: Check highlighted with R & D

## Slide 55: Memory View Basics
To add new memory monitor based on address, click on Add Memory Monitor in Monitors section, provide address or variable name for active debug context, confirm with OK button
To remove memory monitor(s) select monitor(s) from list and click on Remove Memory Monitor
Click on Remove All to remove all monitors
Similar actions are available in context menu

## Slide 56: Software Command Language Overview
Feature | Eclipse | Relevant Tcl Commands
Image selection/file browsing | Image File Browser View | esw –image, -files, functions
Breakpoint Management | Breakpoint View | esw –break, -info break, -cond, -delete, -disable, -enable, -ignore; stop -esw
Watchpoint Management | Breakpoint View | esw –watch,-watchread, -watchwrite, -info, -cond, -delete, -disable, -enable, -ignore; stop -esw
Processor/core Selection | Debug View | esw -focus
Stack Frame Management | Debug View | esw –where,–up/-down/-frame
Control/Stepping Support | Pause/Resume, Stepping Control Buttons | run; ^C interrupt; run –sstep,-snext,-sfinish,-istep

## Slide 57: Software Command Lanuage Overview
Feature | Eclipse | Tcl commands
Source Viewing | Editor Views | esw –list, -source, -substitutepath
Disassembly Viewing | Disassembly View | esw -disassemble
Local Variable Display/Mgmt | Variables View | esw –variables, -parameters, -print, -value, -set, -describe
Expression Viewing/Mgmt | Expressions View | esw –variables, -parameters, print, -value
Register Viewing/Mgmt | Registers View | esw –info component¦register, -print, deposit, value
Memory viewing | Memory View | esw –memread,-memwrite, -examine
System IP register viewing | System View | esw –print,-value, -info; value; deposit

## Slide 58: Software Debugging Features – Command Language Only Features
Feature | Command
Processor Control | esw –halt, -resume, -reset
Scripting Language | xrun –input, -tcl
Gearshift | esw -gearshift
Linux Kernel Module Debug | esw –osname, -debug

## Slide 59
Happy Debugging !!!
Helium

## Slide 61: SW/HW Debug Scenarios
ARM-FM PPU access Hang scenario

## Slide 62: PPU Accesses Hang​
RTL
CPU-FM
CPU Wrapper
Interconnect
PMU-SS
1. Power Management Unit running firmware to initialize SoC
2. SW reads Mailbox Register and hangs as read value != 1
PMU_UP
Utility BFM
SoC Rest of RTL
PPU registers
3. PMU writes to PPU registers
M0 BFM
4. PMU reads PPU status registers and hangs as status != 1
5. Mailbox is not updated and hence SW hangs
1
2
3
4
5
Xcelium
Palladium
Helium

## Slide 63: Hybrid Block Diagram – CPU Wrapper Connections
ufs_card
ufs_host
VirtioP9Device
gic600_bridge
ARMTheodulDynamIQ Wrapper
ARMTheodulDynamIQ_rtlcpu_adapter
chi_tlm2rtl
gic600_bridge
axi_rtl2tlm
RTL
axi_tlm2rtl
ter
AXI Slave Utility BFM
Signal Adapter
CHI Master BFM
AXI Periph Master BFM
SOC RTL
term
Virtual
crouter
loader
pl111_km (lcdc)
GIC600
ARMKleinx1CT
slirp_wrapper
ttymonitor
uart
smc91c111_ethernet
simple_memory
VirtioBlockDevice

## Slide 64: Klein CPU RTL Wrapper in SoC Hybrid
(RTL CPU Wrapper in SoC)
Virtual Platform
CHI-e Master AVIP
cdn_chi_e_rnf_bfm
ARMTheodulDynamIQ Signal Adapter
Crouter
(Virtual Interconnect)
AXI-5 Master AVIP
vr_axi_5_master_bfm
ARMKleinx1CT
Fast Model
ARMTheodulDynamIQ Signal Adapter
axi_tlm2rtl Adapter
chi_tlm2rtl Adapter
AXI-5 Slave AVIP
vr_axi_5_slave_bfm
axi_rtl2tlm Adapter
pvbus_m0
pvbus_periph_m
utility_bus_s
rtl_path
rtl_path
rtl_path
Utility port
M0 Port
MP Port
rtl_path
CPU Signals

## Slide 65: SW/HW Debug using Helium RTL CPU Wrapper Debug Scenario
  Basic Debug Approach
    Connect the Helium SW Debugger and run to the point of failure
    Enable Debug Logs for HW
      Enable AVIP verbosity with knobs
      Enable crouter Logs
    Look for the Transaction Messages printed from AVIP BFM
    Get the waveform around CPU wrapper reaching to/from interconnect or around specific HW Components in SoC Design

## Slide 66: Connect the Helium SW Debugger
TODO:
Read to Mail box Address 0x15900028
Read to Mail box Address 0x15900028 returns value 0, which leads to hang

## Slide 67: Enable AVIP BFM Verbosity
AVIP BFM Verbosity is useful for analyzing the Transaction reaching to/from BFM
Possible configuration for all BFM: {0,100,200,300,400,500} -> {SC_NONE, SC_LOW,SC_MEDIUM,SC_HIGH,SC_FULL,SC_DEBUG}
setenv AVIP_VERBOSITY FULL

## Slide 68: PPU Accesses Hung​
SW was hung at read to MAILBOX_APM_AP (0x15900028)
and was expecting read value = 1
Started debugging transactions happening around 0x15900028 address
With Utility AVIP BFM Verbosity enabled to full, we found the Read Transaction hung at 0x30008 address read
  HW Transactions:
    PMU ROM boot code initiates the PPU (Power Policy Unit) Config transactions to BLOCK1 IP Module.​
    BLOCK1 Module diverts the transactions to CPU Wrapper at Utility Bus Interface targeting to PPU address space.​
    Utility Slave BFM in CPU wrapper will divert the PPU register accesses to Klein CPU Fast Model’s utility bus using AXI_RTL2TLM adaptor.​
    Write transactions to PPU_PWPR (0x03_0000) register followed by read transaction to PPU_PWSR(0x03_0008) register hung
    Read Expected value was not matching​. It was always reading 0x0.
ARM Fast model is NOT working as expected and does not return the expected status by reading PPU_PWSR (0x03_0008) register.
  Using Tcl scripting, implemented the force on AXI Slave BFM Read data path to drive the expected values so that PMU boot code moves ahead and does not hang.​
  PMU_UP signal is asserted after the above adjustment using Tcl scripting​
SW hang issue resolved and Linux was booting successfully
Reason for SW Hang

## Slide 69: Connecting - Helium With an RTL Platform RTL Design Bring-up with Helium SW Debug
Instantiate ABP BFM Adapter
  vd_apb_bfm
Add xrun switches
  -helium
  -esw config:<path/to/esw.config>
Notes: 09/07/21: Check with Ashwin on the available RTL database and also copy the relevant slides from gearshift training. – Done

## Slide 70: AVIP Verbosity Logs
Write Request to 0x30000 received
Valid Write Resp given back
Read Data is always 0
Read Request to 0x30008 received

## Slide 71: PPU Accesses Hang​
Write to 0x3_0000 PPU reg was successful
Read from 0x3_0008 PPU reg hung. Read value is always 0x0.
Choose Starter Platform
Save to Catalog
Add / Remove Virtual Models
Parameter Config / Port Binding
Rewire Interrupt and Memory Map
Add / Remove RTL Stubs
Hybrid Adaptors & RTL Connection
RTL Side changes
Build & Run
Debug

## Slide 72: PPU Accesses Hung​
RTL
CPU-FM
CPU Wrapper
Interconnect
PMU-SS
1. Power Management Unit running firmware to initialize SoC
2. SW Reads Mailbox Register and hangs as read value != 1
PMU_UP
Utility BFM
SoC Rest of RTL
PPU registers
3. PMU writes to PPU registers
M0 BFM
4. PMU reads PPU status registers and Hangs as status != 1
5. Mailbox is not update and Hence SW is Hung
6. Stub the expected value on PPU Reg, allows PMU FW to move ahead. PPU updates the Mailbox.
7. SW Reads Mailbox Register with read value == 1
8
1
2
3
4
5
6
7
8. SW Hang Resolved !!
Xcelium
Palladium
Helium
AVIP Logs

## Slide 73: Connecting - Helium With an RTL Platform

## Slide 74
Connecting the RTL CPU to the Helium debugger
vd_apb_bfm
To Helium debugger
Configuration file:
processor {
...
bfm
{
path tb_top.vd_apb_bfm
type apb
adapter vdi
}
...
Add to existing hybrid TB
RTL
DDR
ROM
SRAM
CPU A76x4
NIC400
GIC600
UART(0-3)
Connecting - Helium With an RTL Platform Connecting the RTL CPU to the Helium debugger